## Slide 1
MASTER THESIS DEFENSE
Battery Re-X Digital Twin and Robotic Sorting System
Computer Vision, SOH Prediction, and Lifecycle Decision Support
Prepared by: Project Owner
Date: 18 June 2026
Project: Battery Re-X Control Twin
AI vision
SOH ML
Re-X route
Unity twin
Project defense deck | public datasets + implemented backend + Unity prototype
01
Notes: Open with the core idea: an automated decision-support pipeline for battery reuse, remanufacturing, recycling, and quarantine.
Emphasize that the project combines computer vision, battery health prediction, backend APIs, and a Unity digital twin.
Suggested animation: title first, then subtitle, then the four pipeline pills.

## Slide 2
PROBLEM
Problem & Motivation
Battery reuse decisions need more than visual inspection.
Motivation slide: circular economy, safety, and sorting risk
02
Waste pressure
Lithium-ion batteries create growing end-of-life streams. Manual sorting is slow and inconsistent when form factor, condition, and route must be assessed together.
Safety risk
Unknown SOH, high temperature, abnormal voltage, and high resistance can turn a reuse candidate into a quarantine case.
Decision complexity
A visual battery type is not enough. A defensible Re-X route needs health data, risk rules, and traceable decisions.
Engineering challenge: combine image-based identification with sensor-based health prediction and robotic sorting.
Notes: Frame the problem around safety and material recovery.
Make clear that the project addresses decision support, not full industrial certification.
Suggested animation: reveal the three problem cards one by one.

## Slide 3
VISION
Project Vision
Battery enters the digital twin, is classified, health-scored, routed, and sorted.
Concept pipeline
03
BAT
Battery intake
Unknown cell on conveyor
CV
AI detection
Cylindrical / pouch / prismatic
ML
SOH prediction
ML from health parameters
RX
Re-X decision
Reuse / reman / recycle / quarantine
3D
Unity twin
State, color, UI panel
BOT
Robot sort
Move to target bin
Design principle
Image determines physical type. Health parameters determine SOH. Safety rules override unsafe cases.
Notes: Walk through the end-to-end pipeline from the unknown battery to the sorting bin.
Stress the separation of responsibilities: CV for form factor, ML for health, rules for safety.
Suggested animation: follow the arrows from left to right.

## Slide 4
DATASET 1
RecyBat24 Image Dataset
Real battery images are used for visual shape classification.
Sources: RecyBat24 subset in data/images; project evaluation report
04
Runtime subset
90 images total: 30 cylindrical, 30 pouch, 30 prismatic.
Public dataset
Use in project
Training/evaluation labels come from folders. Runtime prediction uses image pixels, not filenames.
Implemented
Selected CV model
HOG features + Linear SVM. 5-fold CV accuracy: 98.89%; holdout accuracy: 96.30%.
Evaluated
Notes: Explain that RecyBat24 provides the visible battery form factor data.
Clarify that filenames are not used for runtime prediction, avoiding label leakage.
Mention that the dataset is useful for a prototype but small for production.

## Slide 5
DATASET 2
Battery Aging Data for SOH
Capacity-based SOH training uses NASA-derived battery aging records.
Sources: NASA PCoE Battery Data Set; data/nasa_health/battery_health_lookup.csv
05
Selected data
NASA PCoE Li-ion aging subset extracted from raw .mat files.
Public dataset
Rows used
636 clean discharge-cycle rows from B0005, B0006, B0007, B0018.
Implemented
Target
SOH is calculated from measured capacity divided by rated capacity.
Capacity based
Limit
Current calibration is cylindrical-heavy.
Honest scope
Feature
Meaning
Used by ML?
Source
cycle_count
aging progression
yes
NASA discharge cycles
temperature_c
thermal condition
yes
measured discharge data
internal_resistance_mohm
electrical degradation proxy
yes
nearest impedance cycle
voltage
operating condition
yes
measured discharge data
capacity
SOH label generation
target only
measured capacity
Notes: Explain why NASA was selected: available, capacity-based, and useful for SOH.
Be honest that CALCE and Oxford are future extensions for broader form-factor coverage.
Suggested animation: show selected data, rows, target, limitation.

## Slide 6
DATA BOUNDARY
Why Image Alone Is Not Enough
The image classifies form factor; health measurements estimate SOH.
Design rationale
06
IMG
Image data
Shape, visible form factor, visual capture
TYPE
Battery type
cylindrical / pouch / prismatic
DATA
Health data
cycle, temp, resistance, voltage
SOH
Predicted SOH
ML regression output in %
RX
Re-X decision
SOH + safety rules + type context
A camera can see geometry. It cannot measure electrochemical aging.
Notes: This is a key defense slide.
Make the technical boundary very explicit: image for shape, sensors for health, combined data for route.
Suggested animation: image path, health path, then decision node.

## Slide 7
ARCHITECTURE
System Architecture
Unity, backend AI, passport data, ML SOH, decision rules, and robot sorting.
Project architecture diagram
07
3D
Unity Simulation
conveyor, camera, robot, UI
CAM
Camera Image
uploaded battery photo
CV
AI Vision Backend
HOG + Linear SVM
DB
Battery Passport
id + metadata + log
SIM
Sensor Stage
mock health readings
ML
SOH ML Model
RandomForestRegressor
RX
Re-X Engine
threshold + safety rules
RB
Robot Sort
target bin command
Notes: Explain the system as coupled services rather than a monolithic demo.
Mention the main implemented files if asked: backend/main.py, backend/model.py, backend/ml/soh_model.py, Unity C# scripts.
Suggested animation: top row first, then bottom row.

## Slide 8
COMPUTER VISION
AI Vision Pipeline
Runtime classification uses image pixels, not file names.
Sources: scripts/train_compare_cv_models.py; backend/model.py
08
01
Input image
Unity camera sends selected battery image
02
Preprocessing
resize + grayscale / feature extraction
03
HOG features
shape gradients and edge directions
04
Linear SVM
best evaluated classifier
05
Type output
cylindrical / pouch / prismatic
Model
Feature set
5-fold acc.
Holdout acc.
Status
Linear SVM
HOG
98.89%
96.30%
selected
Logistic Regression
color + shape
96.67%
96.30%
baseline
RBF SVM
hybrid
95.56%
96.30%
compared
Random Forest
color + shape
92.22%
85.19%
rejected
Notes: Walk through the CV pipeline from image to class output.
Emphasize that HOG is appropriate because the classes differ by geometry and edge structure.
Note dataset size as a limitation.

## Slide 9
DIGITAL PASSPORT
Digital Battery Passport
A structured record keeps identity, sensor values, prediction, and decision traceable.
Sources: backend/passport.py; logger outputs
09
BATTERY PASSPORT
battery_id
DXB-REAL-BAT-001
type
cylindrical
cycle_count
430
temperature
31.2 C
voltage
3.72 V
resistance
52.0 mOhm
predicted_soh
94.49%
timestamp
API response time
Why it matters
Passport-style records make each Re-X decision auditable and explainable.
Current prototype
Identity and inspection history are implemented; some fields are simulated because no real BMS is connected.
Mock/simulated
Industrial extension
Replace mock readings with BMS, lab tester, or line-sensor data.
Future work
Notes: Show the passport as the data contract around a battery.
Explain that it is useful for traceability, audit, and operator confidence.
Be clear that some values are mock in this prototype.

## Slide 10
SOH METHOD
SOH Prediction Method
Training uses capacity-derived SOH; inference uses health parameters.
Sources: docs/soh_ml_pipeline.md; scripts/train_soh_models.py
10
SOH (%) = current capacity / rated capacity × 100
Training target
NASA rows include measured capacity. I calculate SOH directly from capacity for supervised learning.
Implemented
Inference inputs
At runtime Unity sends cycle count, temperature, resistance, voltage, and battery type.
Implemented
Prediction output
Backend returns predicted SOH percentage, confidence estimate, risk score, and Re-X route.
Implemented
Important: the model does not predict SOH from image pixels.
Notes: Explain the SOH formula first, then the machine learning inference problem.
Clarify that capacity is available in training but not always at sorting-line inference.
Suggested animation: formula, training target, inference inputs, output.

## Slide 11
MODEL COMPARISON
ML Model Comparison
Five regressors were trained and compared on NASA-derived SOH rows.
Source: outputs/model_evaluation/soh_model_comparison.json
11
Model
MAE
RMSE
R2
MAPE
Notes
RandomForestRegressor
0.5348
0.7761
0.9946
0.6617%
selected; lowest RMSE
SupportVectorRegression
0.6487
0.8919
0.9929
0.8095%
strong small-data model
GradientBoostingRegressor
0.6524
0.9097
0.9926
0.8131%
boosted tree comparison
MLPRegressor
0.8880
1.2145
0.9869
1.0899%
simple neural network
LinearRegression
1.3367
1.7185
0.9737
1.6764%
baseline
Chart: 
| RF | SVR | GBR | MLP | LIN
RMSE | 0.7761 | 0.8919 | 0.9097 | 1.2145 | 1.7185
Implemented
Selected automatically by lowest RMSE, then MAE.
Notes: This slide answers how many models were tested and why.
Mention that XGBoost/LightGBM are optional in the script if installed, but not present in this environment.
Do not overclaim production accuracy because the data is limited.

## Slide 12
DECISION ENGINE
Re-X Decision Engine
The route combines predicted SOH thresholds with safety overrides.
Sources: backend/ml/soh_model.py
12
SOH >= 80%
Reuse
60% <= SOH < 80%
Remanufacture
30% <= SOH < 60%
Recycle
SOH < 30%
Quarantine
Safety override
Missing data, unknown type, abnormal voltage, high resistance, or very high temperature routes to quarantine.
Implemented
Backend output
Route, target bin, risk score, risk level, confidence estimate, and explanation string.
Implemented
Notes: Explain that SOH thresholds are simple and transparent by design.
Stress that safety rules override high SOH when measurements are abnormal.
Suggested animation: reveal thresholds top to bottom, then safety override.

## Slide 13
UNITY TWIN
Unity Digital Twin
The simulation visualizes classification, sensor updates, SOH, route, and bin assignment.
Sources: Unity scripts in Assets/Scripts
13
CV
Shape update
3D battery object changes to classified form factor
UI
Sensor UI
floating panel shows voltage, temp, cycles, resistance
ML
SOH response
backend ML result updates each battery record
3D
Route color
material/bin color follows Re-X decision
Unity element
Status
Source
Notes
Conveyor sequence
Implemented
ConveyorController.cs
classification -> sensors -> ML
Floating panel per battery
Implemented
BatteryFloatingInfoPanel.cs
updates while moving
Selected battery panel
Implemented
BatterySelectionDetailPanel.cs
tap/click details
Sensor values
Simulated
BatteryInspectionClient.cs
mock until hardware exists
Notes: Describe how the Unity scene communicates the AI state visually.
Be honest: the sensor values are mock readings, but the API call and UI update path are implemented.
Mention the per-battery UI panels added to support multiple batteries.

## Slide 14
ROBOTICS
Robotic Sorting Workflow
The robot receives the target bin after the backend Re-X decision.
Sources: RobotSorter.cs; ABBCRBArmController.cs
14
01
Inspection
camera + sensors
02
Decision
SOH + rules
03
Robot pick
gripper action
Reuse
Reman
Recycle
Quarantine
Notes: Explain the robot as the physical output stage of the decision engine.
Clarify that the robot is simulated in Unity, not a real hardware arm yet.
Suggested animation: conveyor, decision gate, robot arc, bins.

## Slide 15
BACKEND API
Backend API
FastAPI endpoints connect Unity, CV, SOH prediction, logs, and passports.
Sources: backend/main.py
15
Endpoint
Purpose
Status
Notes
/classify-battery
image -> type
Implemented
Unity sends camera image; backend returns type and confidence
/predict-soh
health -> SOH + route
Implemented
Unity sends mock sensor values; backend returns Re-X category
/soh-model-metrics
model report
Implemented
Returns selected model and evaluation metrics
/inspect-battery
legacy full inspection
Implemented
Older combined image + lookup flow remains available
/train-soh-model
train via API
Planned
Training currently runs as scripts/train_soh_models.py
{
"cycle_count": 430,
"temperature": 31.2,
"resistance": 0.052,
"voltage": 3.72
}
{
"predicted_soh": 94.49,
"rex_category": "reuse",
"model_used": "RandomForestRegressor"
}
Notes: Show that the backend is not just a placeholder; routes exist and were smoke-tested.
Be clear that train-soh-model is not an API endpoint yet; training is a script.
Suggested animation: request JSON, arrow, response JSON.

## Slide 16
CASE STUDY
Example End-to-End Case
A real API smoke test routes BAT_001 to reuse.
Source: backend /predict-soh smoke test
16
BAT_001
Type
Cylindrical
Cycle Count
430
Temperature
31.2 C
Resistance
0.052 ohm
Voltage
3.72 V
Predicted SOH
94.49%
Decision
Reuse
Target Bin
reuse_bin
IN
Input
image classified as cylindrical + sensor data
ML
ML prediction
RandomForestRegressor predicts SOH 94.49%
OUT
Unity output
green material + reuse bin command
Notes: Use this as the concrete proof that the endpoint returns a complete Re-X decision.
Say this is a smoke-test example, not a physical battery measurement.
Suggested animation: input, ML prediction, Unity output.

## Slide 17
RESULTS
Results / Demo Outputs
Current outputs combine model evaluation and backend smoke-test routing.
Sources: model reports and backend smoke tests
17
Battery ID
Type
SOH
Re-X Category
Risk
Unity/Backend Output
BAT_001
cylindrical
94.49%
reuse
low
reuse_bin / green
BAT_002
pouch
94.52%
reuse
low
reuse_bin / green
BAT_003
prismatic
67.91%
remanufacture
medium
remanufacture_bin / yellow
BAT_004
pouch
94.60%
quarantine
high
safety override: high_temperature
Vision result
Selected CV model: HOG + Linear SVM, 98.89% mean 5-fold CV accuracy.
Evaluated
SOH result
Selected SOH model: Random Forest, RMSE 0.7761 SOH percentage points.
Evaluated
Demo video
No project video file found. Insert Unity demo recording here after capture.
Placeholder
Notes: Explain that these are software validation outputs, not industrial validation results.
The quarantine case demonstrates the safety override logic.
The video slot is intentionally marked as a placeholder because no video exists in the project.

## Slide 18
STATUS
Implementation Status
Each claim is labeled by current evidence in the repository.
Sources: project files and generated model artifacts
18
Feature
Status
Evidence/File
Notes
RecyBat24 image subset
Implemented
data/images; data/image_sources.csv
90 images, balanced classes
CV classifier
Implemented
backend/model.py; trained_models/battery_type_classifier.joblib
HOG + Linear SVM
SOH ML model
Implemented
backend/ml/soh_model.py; soh_predictor.joblib
Random Forest selected
Mock health sensors
Simulated
BatteryInspectionClient.cs
Unity generates sensor values
Re-X routing
Implemented
backend/ml/soh_model.py
SOH thresholds + safety rules
Unity digital twin
Implemented
Assets/Scripts/*.cs
visual workflow and panels
Real BMS/robot hardware
Planned
future work
not connected in prototype
Defense rule: implemented means code/artifact exists; simulated means software behavior exists without real hardware; planned means future scope.
Notes: Use this slide if an examiner asks what is actually implemented.
Avoid exaggeration: real hardware and BMS are planned, not implemented.
Suggested animation: none; keep this slide clear and static.

## Slide 19
LIMITATIONS
Limitations
The prototype is technically functional, but not an industrial validation system yet.
Project limitations
19
Image cannot determine SOH
Images support shape detection and visible condition only. SOH requires health measurements.
Dataset generalization
NASA SOH training data is cylindrical-heavy and limited to 636 clean rows.
Mock health data
Unity uses random mock sensor inputs because no real sensor/BMS data stream is connected.
Safety certification
Industrial routing would require validated safety rules, calibration, and hazardous material procedures.
Robot hardware
The sorting workflow is simulated in Unity; real robot control is future work.
Uncertainty
Confidence is based on residual error estimate; production uncertainty needs stronger calibration.
Notes: Use this slide to build examiner trust.
State limitations clearly before future work.
Suggested animation: reveal limitations in two rows.

## Slide 20
FUTURE WORK
Future Work
The next stage is real sensor integration, broader data, and hardware-grade robotics.
Future roadmap
20
Real BMS integration
replace mock sensor data
Future work
Chemistry-specific models
NMC / LFP / LCO calibration
Future work
CALCE + Oxford expansion
pouch/prismatic aging coverage
Future work
ROS 2 / Gazebo
robot control stack integration
Future work
Thermal / X-ray inspection
safety and internal damage sensing
Future work
Edge AI deployment
factory-line latency and robustness
Future work
Notes: Present future work as a credible engineering roadmap.
Tie each item back to a limitation from the previous slide.
Suggested animation: one roadmap card at a time.

## Slide 21
CONCLUSION
Conclusion
A proof-of-concept for circular battery lifecycle decision support.
Project conclusion
21
I designed and implemented a modular Re-X decision pipeline that connects vision, health prediction, backend reasoning, Unity visualization, and robotic sorting logic.
Technically honest
Image = shape; health data = SOH; route = ML + safety rules.
Working prototype
Models, API endpoints, Unity panels, and sorting flow are integrated.
Clear next step
Connect real BMS/sensor data and extend aging datasets.
Notes: Summarize the project as an integrated proof-of-concept.
End on the clear contribution: traceable lifecycle decision support.
Suggested animation: main sentence, then three cards.

## Slide 22
Q&A
Questions?
Battery Re-X Digital Twin and Robotic Sorting System
CV + SOH ML + Re-X Decision + Unity Digital Twin
Q&A | References: RecyBat24, NASA PCoE, project repository artifacts
22
Notes: Invite questions and be ready to defend the separation between image classification and SOH prediction.
If asked about limitations, point back to slides 18 and 19.
If asked about the next experiment, propose real BMS data integration and CALCE/Oxford expansion.